## Slide 1: COMN - Computer Communications and Networks Coursework Introduction: SDN
Michio Honda
School of Informatics
University of Edinburgh
27/01/2021
Text version is also available at https://git.ecdf.ed.ac.uk/mhonda/comn_cw/blob/master/sdn/introduction.md
Notes: ‹#›

## Slide 2: SDN and OpenFlow
SDN
  Centralised network architecture
  Control plane
    Policy and management
  Data (forwarding) plane
    Packet forwarding
OpenFlow
  De facto protocol to achieve SDN
Controller
Switch
Update forwarding rules

## Slide 3: What is a Flow?
A group of packets in various meaningful form, like
  Packets with the same source-destination MAC address pair
  TCP packets with the same four tuple (<src_ip><dst_ip><src_port><dst_port>)

## Slide 4: OpenFlow in action
A switch forwards packets that do not match any existing flows to the controller
The controller makes decision what to do for this packet, like
  Drop
  Insert the flow to the switch so that the packets that match this flow do not go to the controller anymore
Controller
Switch
Insert <in_port=1 src_mac=a0:bc..cb, dst_mac=1c:4d..73> action=out:2
1st pkt
2nd pkt in the same flow

## Slide 5: Mininet and Ryu
Mininet
  A network emulator that runs in a single (virtual) machine
Ryu
  Python framework to implement OpenFlow controllers
Both are pre-installed in our VM

## Slide 6: Running Ryu and Mininet
(In the VM)
vagrant@ubuntu-focal:~/comn_cw/sdn$ ryu-manager l2learn.py
loading app l2learn.py
loading app ryu.controller.ofp_handler
instantiating app l2learn.py of L2Learn14
instantiating app ryu.controller.ofp_handler of OFPHandler
(In another window)
vagrant@ubuntu-focal:~$ sudo mn --topo single,3 --mac --controller remote
*** Creating network
*** Adding controller
Connecting to remote controller at 127.0.0.1:6653
*** Adding hosts:
h1 h2 h3
*** Adding switches:
s1
*** Adding links:
(h1, s1) (h2, s1) (h3, s1)
*** Configuring hosts
h1 h2 h3
*** Starting controller
c0
*** Starting 1 switches
s1 ...
*** Starting CLI:
mininet>
h1
s1
h2
h3
c0

## Slide 7: Executing a UNIX command
Executing a UNIX command
mininet> h2 ping -c 1 h1
PING 10.0.0.1 (10.0.0.1) 56(84) bytes of data.
64 bytes from 10.0.0.1: icmp_seq=1 ttl=64 time=0.175 ms
--- 10.0.0.1 ping statistics ---
1 packets transmitted, 1 received, 0% packet loss, time 0ms
rtt min/avg/max/mdev = 0.175/0.175/0.175/0.000 ms
Some commands do not need to specify the host
mininet> pingall
*** Ping: testing ping reachability
h1 -> h2 h3
h2 -> h1 h3
h3 -> h1 h2
*** Results: 0% dropped (6/6 received)

## Slide 8: Understanding controler behavior
(stop the ryu controller (ctrl+c) and exit from Mininet (type “exit”)
Let’s put a print() in the function called every time the controller receives a packet
vagrant@ubuntu-focal:~/comn_cw/sdn$ vi l2learn.py
...
@set_ev_cls(ofp_event.EventOFPPacketIn, MAIN_DISPATCHER)
def _packet_in_handler(self, ev):
print(in_port, pkt) # add this line
msg = ev.msg
...
Then run Ryu-controller and Mininet again, and do pingall
  You will see packets received at the ryu-controller output

## Slide 9: Understanding L2 Learning switch in Ryu
(l2learn.py)
@set_ev_cls(ofp_event.EventOFPPacketIn, MAIN_DISPATCHER)
def _packet_in_handler(self, ev):
1 msg = ev.msg
2 in_port, pkt = (msg.match['in_port'], packet.Packet(msg.data))
3 dp = msg.datapath
4 ofp, psr, did = (dp.ofproto, dp.ofproto_parser, format(dp.id, '016d'))
5 eth = pkt.get_protocols(ethernet.ethernet)[0]
6 dst, src = (eth.dst, eth.src)
7 self.ht.setdefault(did, {})
8 he = self.ht[did] # shorthand
9 he[src] = in_port
10 out_port = he[dst] if dst in he else ofp.OFPP_FLOOD
Line 9: First create a hash table entry for the source MAC
Line 10: Decide the output port(s) based on the existence of the destination MAC address entry

## Slide 10: Understanding L2 Learning switch in Ryu
(l2learn.py)
...
11 acts = [psr.OFPActionOutput(out_port)]
12 if out_port != ofp.OFPP_FLOOD:
13 mtc = psr.OFPMatch(in_port=in_port, eth_dst=dst, eth_src=src)
14 self.add_flow(dp, 1, mtc, acts, msg.buffer_id)
15 if msg.buffer_id != ofp.OFP_NO_BUFFER:
16 return
17 data = msg.data if msg.buffer_id == ofp.OFP_NO_BUFFER else None
18 out = psr.OFPPacketOut(datapath=dp, buffer_id=msg.buffer_id,
19 in_port=in_port, actions=acts, data=data)
20 dp.send_msg(out)
Line 11: Generate a list of action list (just output in this case)
Line 12-: If the correct output port has been identified (Line 12), insert the flow entry (matches to src/dst MAC addresses and input port, as seen in Line 13) to the switch (Line 14). Then the controller applies the packet action (Line 18-20)

## Slide 11: Summary
We learned Mininet and Ryu
SDN is a popular networking research topic:
  Flow management technique [1]
  Controller fault Tolerance [2]
  Dataplane abstraction [3]
  Host switch [4]
Many interesting papers at ACM SOSR and SIGCOMM, and USENIX NSDI
[1] https://conferences.sigcomm.org/sigcomm/2011/papers/sigcomm/p254.pdf
[2] https://www.cs.princeton.edu/~mfreed/docs/ravana-sosr15.pdf
[3] https://www.sigcomm.org/sites/default/files/ccr/papers/2014/July/0000000-0000004.pdf
[4] https://www.usenix.org/system/files/conference/nsdi17/nsdi17-firestone.pdf